Notice to Mariners No. 7 of 2009

Thursday, February 12, 2009

South Australia - River Murray - Goolwa Channel

Mariners are advised that some of the channel markers in the main channel at Goolwa from the Murray Mouth to the Goolwa Barrage have been moved and several additional beacons have been installed.

The beacons have been renumbered in line with convention i.e. starboard with odd numbers and port with even numbers. Beacons have been fitted with corresponding coloured reflective bands to assist at night.

Two Special Marks (yellow X topmark) have been positioned on either end of an area of shoaling within the channel just downstream of the Number 19 Boat Ramp and adjacent to Beacon 7. These markers have been fitted with yellow flashing lights, the upstream light has a sequence of Q4(10s) the downstream light a sequence of Q6(10s). Passage is possible on either side, however mariners are advised of their obligation to keep to the starboard side when navigating in narrow channels.

Commencing from the Murray Mouth the locations have been accurately determined and positions and new numbers are indicated below.

| New No. (Type) | Old No. | Zone 54H | Latitude | Longitude |
| --- | --- | --- | --- | --- |
|  |  | Easting | Northing |  |  |
| 1 (S) | 4 | 305948 | 6064405 | 35° 32' 42.09"S | 138° 51' 33.54"E |
| 2 (P) | New | 307360 | 6063941 | 35° 32' 58.13"S | 138° 52' 29.18"E |
| 3 (S) | 6 | 305651 | 6064580 | 35° 32' 36.20"S | 138° 51' 21.90"E |
| 4 (P) | 11 | 307058 | 6063955 | 35° 32' 57.48"S | 138° 52' 17.20"E |
| 5 (S) | 8 | 304516 | 6065545 | 35° 32' 04.10"S | 138° 50' 37.66"E |
| 6(P) | 13 | 304933 | 6065070 | 35° 32' 19.79"S | 138° 50' 53.80"E |
| 7 (S) | 10 | 303608 | 6065934 | 35° 31' 50.84"S | 138° 50' 01.98"E |
| 8 (P) | New | 304717 | 6065254 | 35° 32' 13.70"S | 138° 50' 45.42"E |
| 9 (S) | 12 | 302814 | 6066180 | 35° 31' 42.30"S | 138° 49' 30.69"E |
| 10 (P) | 15 | 304170 | 6065501 | 35° 32' 05.27"S | 138° 50' 23.90"E |
| 11 (S) | 14 | 302253 | 6066376 | 35° 31' 35.52"S | 138° 49' 08.61"E |
| 12 (P) | 17 | 303692 | 6065645 | 35° 32' 00.29"S | 138° 50' 05.07"E |
| 14 (P) | 19 | 303036 | 6065919 | 35° 31' 50.91"S | 138° 49' 39.28"E |
| 16 (P) | 21 | 302233 | 6066183 | 35° 31' 41.78"S | 138° 49' 07.64"E |
| 18 (P) | 23 | 301625 | 6066340 | 35° 31' 36.24"S | 138° 48' 43.65"E |
| Special Mark | New | 303442 | 6065884 | 35° 31' 52.35"S | 138° 49' 55.34"E |
| Special Mark | New | 303575 | 6065841 | 35° 31' 53.83"S | 138° 50' 00.60"E |

Mariners are reminded that they should take care to familiarise themselves with the realigned channel and additional markers.

Notice to Mariners No. 42 of 2009

Tuesday, August 04, 2009

SOUTH AUSTRALIA - RIVER MURRAY - GOOLWA CHANNEL AND LAKE ALEXANDRINA

Mariners are advised that many of the navigation beacons from the Goolwa Barrage to Brinkley have been moved. Additionally there are a number of new beacons.

The beacons all have new three dimensional top marks and have been renumbered (see Notice 7 of 2009).

The beacons from the Goolwa Barrage to Clayton have been lit after the completion of a trial in the area. From the Goolwa Barrage to Narnu Bay (Beacon No 44) the lights flash every four seconds and are synchronised. The last beacon of the synchronised lights will flash twice each 4 seconds. The beacons from Narnu Bay to Clayton are in three sections to assist mariners to determine approximate location along the channel. Each section end is marked with a distinctive flash pattern. All other beacons are unlit and details are listed hereunder.

| Bcn No. | Old No. | Type | Action | Zone 54H | Latitude | Longitude | Flash Pattern |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Easting | Northing |  |  |  |
| 13 |  | Stbd | New | 301094 | 6066778 | 35°31'21.67"S | 138°48'22.95"E | FLG4s |
| 15 | 16 | Stbd |  | 300914 | 6067004 | 35°31'14.18"S | 138°48'16.04"E | FLG4s |
| 15A |  | Stbd | New | 300526 | 6067402 | 35°31'01.01"S | 138°48'01.00"E | FLG4s |
| 17 |  | Stbd | New | 299842 | 6067918 | 35°30'43.78"S | 138°47'34.32"E | FLG4s |
| 19 |  | Stbd | New | 299471 | 6067948 | 35°30'42.53"S | 138°47'19.60"E | FLG4s |
| 20 | 23A | Port |  | 301124 | 6066440 | 35°31'32.65"S | 138°48'23.85"E | FLR4s |
| 21 | 18 | Stbd | Moved | 299285 | 6068114 | 35°30'37.00"S | 138°47'12.38"E | FLG4s |
| 22 | 25 | Port | Moved | 300729 | 6066916 | 35°31'16.92"S | 138°48'08.61"E | FLR4s |
| 23 |  | Stbd | New | 299247 | 6068393 | 35°30'27.95"S | 138°47'11.11"E | FLG4s |
| 24 |  | Port | New | 300483 | 6067316 | 35°31'03.77"S | 138°47'59.21"E | FLR4s |
| 25 | 20 | Stbd | Moved | 299810 | 6069312 | 35°29'58.55"S | 138°47'34.28"E | FLG4s |
| 26 | 27 | Port |  | 300339 | 6067440 | 35°30'59.64"S | 138°47'53.61"E | FLR4s |
| 27 | 22 | Stbd | Moved | 300311 | 6069534 | 35°29'51.69"S | 138°47'54.33"E | FLG4s |
| 28 | 29 | Port | Moved | 300064 | 6067597 | 35°30'54.34"S | 138°47'42.83"E | FLR4s |
| 29 | 24 | Stbd | Moved | 300807 | 6069696 | 35°29'46.82"S | 138°48'14.15"E | FLG4s |
| 30 |  | Port | New | 299834 | 6067801 | 35°30'47.56"S | 138°47'33.90"E | FLR4s |

| 31 | 26 | Stbd |  | 301121 | 6069692 | 35°29'47.16"S | 138°48'26.60"E | FLG4s |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 32 | 31 | Port |  | 299589 | 6067859 | 35°30'45.52"S | 138°47'24.23"E | FLR4s |
| 33 | 28 | Stbd | Moved | 301522 | 6069653 | 35°29'48.70"S | 138°48'42.48"E | FLG4s |
| 34 | 35A | Port |  | 300620 | 6069794 | 35°29'43.48"S | 138°48'06.85"E | FLR4s |
| 35 | 30 | Stbd | Moved | 302482 | 6069532 | 35°29'53.33"S | 138°49'20.47"E | FLG4s |
| 36 | 35 | Port |  | 301852 | 6069758 | 35°29'45.53"S | 138°48'55.69"E | FLR4s |
| 37 | 32 | Stbd | Moved | 302887 | 6069445 | 35°29'56.43"S | 138°49'36.45"E | FLG4s |
| 38 | 37 | Port | Moved | 303455 | 6069418 | 35°29'57.70"S | 138°49'58.97"E | FLR4s |
| 39 | 34 | Stbd | Moved | 303274 | 6069339 | 35°30'00.15"S | 138°49'51.71"E | FLG4s |
| 40 | 39 | Port | Moved | 303804 | 6069404 | 35°29'58.42"S | 138°50'12.79"E | FLR4s |
| 41 | 36 | Stbd | Moved | 303753 | 6069292 | 35°30'02.01"S | 138°50'10.67"E | FLG4s |
| 42 | 41 | Port | Moved | 304276 | 6069562 | 35°29'53.64"S | 138°50'31.64"E | FLR4s |
| 43 | 38 | Stbd | Moved | 304173 | 6069404 | 35°29'58.67"S | 138°50'27.42"E | FLG4s |
| 44 | 43 | Port | Moved | 305118 | 6069930 | 35°29'42.29"S | 138°51'05.38"E | FLR(2)4s |
| 45 | 40 | Stbd | Moved | 304812 | 6069667 | 35°29'50.60"S | 138°50'52.99"E | FLG4s |
| 46 | 45 | Port | Moved | 305810 | 6070360 | 35°29'28.85"S | 138°51'33.20"E | VQR(3)5s |
| 47 | 42 | Stbd | Moved | 305337 | 6069911 | 35°29'43.06"S | 138°51'14.02"E | VQG(3)5s |
| 48 | 47 | Port | Moved | 306437 | 6070483 | 35°29'25.27"S | 138°51'58.14"E | VQR(3)5s |
| 49 | 44 | Stbd | Moved | 305804 | 6070184 | 35°29'34.53"S | 138°51'32.81"E | VQG(3)5s |
| 50 | 49 | Port | Moved | 307045 | 6070510 | 35°29'24.82"S | 138°52'22.28"E | QR(3)6s |
| 51 | 46 | Stbd | Moved | 306214 | 6070307 | 35°29'30.83"S | 138°51'49.15"E | VQG(3)5s |
| 52 | 51 | Port | Moved | 307945 | 6070614 | 35°29'22.08"S | 138°52'58.07"E | FLR(2+1)6s |
| 53 | 48 | Stbd |  | 306732 | 6070339 | 35°29'30.17"S | 138°52'09.73"E | VQG(3)5s |
| 54 | 53 | Port |  | 308883 | 6070646 | 35°29'21.69"S | 138°53'35.29"E | FLR(2+1)6s |
| 55 | 50 | Stbd |  | 307229 | 6070374 | 35°29'29.35"S | 138°52'29.46"E | FLG(2+1)6s |
| 56 | 55 | Port | Moved | 309663 | 6070397 | 35°29'30.30"S | 138°54'06.03"E | QR(4)6s |
| 57 | 52 | Stbd | Moved | 307893 | 6070473 | 35°29'26.63"S | 138°52'55.89"E | FLG(2+1)6s |
| 58 | 57 | Port | Moved | 309868 | 6070263 | 35°29'34.80"S | 138°54'14.03"E | QR(2)5s |
| 59 | 54 | Stbd | Moved | 308625 | 6070439 | 35°29'28.22"S | 138°53'24.89"E | FLG(2+1)6s |
| 60 | 59 | Port | Moved | 310161 | 6069993 | 35°29'43.77"S | 138°54'25.43"E | QR(2)5s |

| 61 | 56 | Stbd | Moved | 309219 | 6070376 | 35°29'30.68"S | 138°53'48.41"E | FLG(2+1)6s |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 62 | 61 | Port | Moved | 310452 | 6069808 | 35°29'49.97"S | 138°54'36.82"E | QR(2)5s |
| 63 | 58 | Stbd | Moved | 309794 | 6070208 | 35°29'36.53"S | 138°54'11.07"E | QG(2)5s |
| 64 |  | Port | New | 310692 | 6069785 | 35°29'50.87"S | 138°54'46.34"E | QR(2)5s |
| 65 | 60 | Stbd | Moved | 310086 | 6069921 | 35°29'46.03"S | 138°54'22.39"E | QG(2)5s |
| 66 | 63 | Port | Moved | 312293 | 6069073 | 35°30'15.07"S | 138°55'49.23"E |  |
| 67 | 62 | Stbd | Moved | 311315 | 6069640 | 35°29'55.99"S | 138°55'10.92"E | QG(5)7s |
| 68 | 65 | Port | Moved | 313310 | 6068429 | 35°30'36.65"S | 138°56'29.05"E |  |
| 69 | 64 | Stbd |  | 313425 | 6068103 | 35°30'47.29"S | 138°56'33.36"E |  |
| 70 | 67 | Port |  | 314115 | 6068064 | 35º30'49.02"S | 138º57'00.68"E |  |
| 71 | 66 | Stbd |  | 313973 | 6067909 | 35º30'53.95"S | 138º56'54.92"E |  |
| 72 | 69 | Port |  | 314696 | 6067951 | 35º30'53.09"S | 138º57'23.65"E |  |
| 73 | 68 | Stbd |  | 314703 | 6067835 | 35º30'56.85"S | 138º57'23.85"E |  |
| 74 | 71 | Port |  | 315141 | 6067871 | 35º30'55.98"S | 138º57'41.23"E |  |
| 75 | 70 | Stbd |  | 315403 | 6067622 | 35º31'04.23"S | 138º57'51.43"E |  |
| 76 | 73 | Port |  | 316488 | 6067438 | 35º31'10.92"S | 138º58'34.33"E |  |
| 77 |  | Stbd | New | 315739 | 6067520 | 35°31'07.76"S | 138°58'04.68"E |  |
| 78 | 75 | Port |  | 317455 | 6067007 | 35°31'25.56"S | 138°59'12.35"E |  |
| 79 | 72 | Stbd | Moved | 316108 | 6067280 | 35°31'15.79"S | 138°58'19.12"E |  |
| 80 | 77 | Port |  | 318695 | 6067202 | 35º31'20.05"S | 139º00'01.72"E |  |
| 81 | 74 | Stbd |  | 316518 | 6067000 | 35º31'25.17"S | 138º58'35.16"E |  |
| 82 | 79 | Port |  | 319394 | 6067439 | 35º31'12.81"S | 139º00'29.66"E |  |
| 83 | 76 | Stbd | Moved | 317280 | 6066658 | 35°31'36.77"S | 138°59'05.11"E |  |
| 84 | 81 | Port |  | 320579 | 6067605 | 35º31'08.20"S | 139º01'16.81"E |  |

| 85 | 78 | Stbd | Moved | 317880 | 6066592 | 35°31'39.30"S | 138°59'28.87"E |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 85 | 83 | Port |  | 322264 | 6068419 | 35º30'42.90"S | 139º02'24.31"E |  |
| 87 | 80 | Stbd |  | 318623 | 6066459 | 35º31'44.09"S | 139º02'24.31"E |  |
| 88 | 85 | Port |  | 324534 | 6070355 | 35º29'41.54"S | 138º59'58.27"E |  |
| 89 | 82 | Stbd |  | 319391 | 6066057 | 35º31'57.65"S | 139º00'28.44"E |  |
| 90 | 87 | Port | Moved | 326892 | 6072062 | 35°28'47.66"S | 139°05'30.72"E |  |
| 91 | 84 | Stbd |  | 320034 | 6065838 | 35º32'05.18"S | 139º00'53.76"E |  |
| 92 | 89 | Port |  | 350324 | 6081979 | 35º23'39.59"S | 139º21'06.76"E |  |
| 93 | 86 | Stbd |  | 320720 | 6065149 | 35º32'27.96"S | 139º01'20.42"E |  |
| 94 | 91 | Port |  | 350292 | 6082350 | 35º23'27.52"S | 139º21'05.72"E |  |
| 95 | 88 | Stbd | Moved | 324508 | 6068127 | 35°30'53.81"S | 139°03'53.10"E |  |
| 96 | 93 | Port |  | 350372 | 6082967 | 35º23'07.56"S | 139º21'09.31"E |  |
| 97 | 90 | Stbd | Moved | 331096 | 6071418 | 35°29'11.14"S | 139°08'17.01"E |  |
| 98 | 95 | Port |  | 350519 | 6083226 | 35º22'59.23"S | 139º21'15.30"E |  |
| 99 | 92 | Stbd |  | 337110 | 6073330 | 35º28'12.74"S | 139º12'16.92"E |  |
| 100 | 97 | Port |  | 350654 | 6083474 | 35º22'51.24"S | 139º21'20.81"E |  |
| 101 | 94 | Stbd | Moved | 342807 | 6075860 | 35º26'53.95"S | 139º16'04.64"E |  |
| 102 | 99 | Port |  | 350893 | 6083801 | 35º22'40.77"S | 139º21'30.49"E |  |
| 103 | 96 | Stbd |  | 348619 | 6079680 | 35º24'53.25"S | 139º19'57.64"E |  |
| 104 | 101 | Port |  | 350971 | 6084156 | 35º22'29.30"S | 139º21'33.83"E |  |
| 105 | 98 | Stbd |  | 350483 | 6082183 | 35º23'33.05"S | 139º21'13.19"E |  |
| 106 | 103 | Port | Moved | 351117 | 6084753 | 35º22'09.99"S | 139º21'39.99"E |  |
| 107 | 100 | Stbd |  | 350490 | 6082563 | 35º20'20.72"S | 139º21'13.73"E |  |
| 109 | 102 | Stbd |  | 350830 | 6082970 | 35º23'07.70"S | 139º21'27.46"E |  |
| 111 | 104 | Stbd |  | 351069 | 6083480 | 35º22'51.29"S | 139º21'37.25"E |  |
| 113 | 106 | Stbd |  | 351195 | 6084048 | 35º22'32.90"S | 139º21'42.60"E |  |
| 115 | 108 | Stbd |  | 351312 | 6084585 | 35º22'15.56"S | 139º21'47.59"E |  |
| 117 | 110 | Stbd |  | 351486 | 6085052 | 35º22'00.04"S | 139º21'47.90"E |  |
|  | At Milang a port hand beacon has been placed at the end of a sand bar which protrudes from Reedy Island toward the Milang Jetty. |  |
|  | Port (Milang) | New | 316622 | 6079600 | 35°24'36.49"S | 138°58'49.51"E |  |

Notice to Mariners No.41 of 2009

Tuesday, August 04, 2009

SOUTH AUSTRALIA - RIVER MURRAY - MUNDOO CHANNEL

Mariners are advised that a channel marker in the Mundoo Channel has been moved and an additional beacon has been installed. Also two starboard buoys have been placed opposite the shacks on the Mundoo Channel. Three dimensional topmarks have been installed and the markers numbered. The positions of all Mundoo Channel beacons are listed hereunder;

| Channel Marker | Action | Zone 54H | Latitude | Longitude |
| --- | --- | --- | --- | --- |
|  |  | Easting | Northing |  |  |
| M1 | Moved | 309733 | 6063308 | 35°33'20.31"S | 138°54'02.84"E |
| M2 | New | 309713 | 6063080 | 35°33'27.69"S | 138°54'01.84"E |
| M3 |  | 308674 | 6064231 | 35°32'49.64"S | 138°53'21.58"E |
| M4 | Moved | 309741 | 6063159 | 35°33'25.14"S | 138°54'03.00"E |
| M6 |  | 309699 | 6063321 | 35°33'19.87"S | 138°54'01.46"E |
| M8 |  | 309692 | 6063384 | 35°33'17.81"S | 138°54'01.27"E |
| M10 |  | 309650 | 6063649 | 35°33'09.18"S | 138°53'59.80"E |
| M12 |  | 309001 | 6064346 | 35°32'46.15"S | 138°53'34.63"E |
| Buoy | New | 308293 | 6064325 | 35°32'46.34"S | 138°53'06.54"E |
| Buoy | New | 308101 | 6064488 | 35°32'40.90"S | 138°52'59.05"E |

Notice to Mariners No. 40 of 2009

Tuesday, August 04, 2009

SOUTH AUSTRALIA - RIVER MURRAY - COORONG CHANNEL

Mariners are advised that a channel marker in the main channel from the Murray Mouth into the Coorong has been moved and an additional beacon has been installed. The port beacons beyond the new beacon number 10 have been renumbered.

The channel upstream of Pelican Point beyond Beacon 19 has been marked with 5 starboard buoys as listed below.

| Channel Marker | Old No. | Action | Zone 54H | Latitude | Longitude |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Easting | Northing |  |  |
| 8 |  | moved | 317987 | 6060206 | 35°35'06.54"S | 138°59'27.95"E |
| 10 |  | new | 318086 | 6060112 | 35°35'09.64"S | 138°59'31.81"E |
| 12 | 10 |  | 318210 | 6060079 | 35°35'10.78"S | 138°59'36.73"E |
| 14 | 12 |  | 318763 | 6060047 | 35°35'12.20"S | 138°59'58.65"E |
| 16 | 14 |  | 319440 | 6059724 | 35°35'23.13"S | 139°00'25.26"E |
| 18 | 16 |  | 319757 | 6059575 | 35°35'28.18"S | 139°00'37.76"E |
| Buoy |  | new | 321764 | 6058232 | 35°36'13.04"S | 139°01'56.38"E |
| Buoy |  | new | 322174 | 6058008 | 35°36'20.56"S | 139°02'12.48"E |
| Buoy |  | new | 322581 | 6057797 | 35°36'27.69"S | 139°02'28.48"E |
| Buoy |  | new | 322982 | 6057539 | 35°36'36.31"S | 139°02'44.21"E |
| Buoy |  | new | 323352 | 6057284 | 35°36'44.81"S | 139°02'58.70"E |